## Slide 1
ATP 2026 / ENEC CHALLENGE
A post-alert response for seasonal jellyfish blooms
A testable, two-layer concept focused on marine-life protection and less manual response.
TEAM Bashger Aljneibi · Keyal Doshi · Abdul Fattah Mohammed · Abdul Bari Mohammed
Notes: Proposal concept. The supplied MARLIN image is an illustrative visual, not a site-validated layout.
Challenge brief: https://challengeon.atrc.ae/en/challenges/atp2026/pages/enec-challenge-statement?lang=en

## Slide 2
01 / EXECUTIVE BRIEF
Two physical layers, one simple objective
Respond after the existing bloom alert—guide, collect gently, and keep the intake screens as backup.
97.5%
delivered to a hypothetical supervised receiver
2.5% remained uncaptured in the v4 reference run.
SCREENING RESULT
A model outcome under stated assumptions—not a field catch-rate claim.
01
Outer guide
Primary interception; guided conveyance to a wet receiver.
02
Second guide
Independent reserve line for bloom that passes the first.
03
Measured response
Operate after the ENEC alert; local interlocks bound automation.
TEAM Bashger Aljneibi · Keyal Doshi · Abdul Fattah Mohammed · Abdul Bari Mohammed
Reference run: 12 m assumed depth · 200 m corridor · 1,200 kg/h synthetic arrival · 8 h simulation.
MARLIN / ATP 2026 • ENEC CHALLENGE
02
Notes: The v4 reference result is taken from the project’s local screening report: workbench/v4/output/RUN_REPORT.md. The model reports 2.50% uncaptured and 97.50% delivered to its hypothetical supervised shore-receiving step for the reference scenario.
The model uses synthetic bloom input and uncalibrated contact probabilities; it is not a verified field performance estimate.
Official challenge scope: https://challengeon.atrc.ae/en/challenges/atp2026/pages/enec-challenge-statement?lang=en

## Slide 3
02 / CHALLENGE FRAMING
The hard part begins after the alert
MARLIN is a bloom-response concept, not a replacement for ENEC’s offshore warning program.
A large bloom is a moving, high-volume load.
Manual clearing can require sustained field effort. Any new barrier or collector must also avoid shifting risk onto other marine life or water flow.
01
Reduce repeated manual work
Automate routine conveyance and monitoring, with operators retaining oversight.
02
Protect marine life
Measure bycatch, injury, escape routes, and handling outcomes before scaling.
03
Handle continuous volume
Size collection, buffers, and response capacity for bloom loads—not isolated animals.
Challenge brief: post-alert management • marine-life protection • lower manual intervention • cost-conscious scaling.
MARLIN / ATP 2026 • ENEC CHALLENGE
03
Notes: The official ATP 2026 ENEC brief says ENEC already has an offshore bloom early-warning program and asks for sustainable management after an alert. It emphasizes harm minimization, practicality, reduced manual intervention, cost-conscious scalability, evidence/assumptions, and large continuous blooms.
Source: https://challengeon.atrc.ae/en/challenges/atp2026/pages/enec-challenge-statement?lang=en

## Slide 4
03 / SYSTEM DESIGN
Two interception layers; one controlled collection route
Conceptual cross-section only. Final placement, coverage, skirt depth, and collection points require site data.
SEA SURFACE
SEABED / clearance and anchoring must be surveyed
BLOOM APPROACH
›
›
›
Illustrative cohort markers
Optional seabed airlift / bubble curtain
trial-only; off in reference result
OUTER GUIDE
SECOND GUIDE
surface-to-near-bed skirt
surface-to-near-bed skirt
GENTLE WET
CONVEYOR + LIFT
GENTLE WET
CONVEYOR + LIFT
SUPERVISED
WET RECEIVER
→
Existing intake screens remain independent backup
Current →
The model assumes 12 m water depth; actual bathymetry and side/bottom escape paths are unknown.
MARLIN / ATP 2026 • ENEC CHALLENGE
04
Notes: The cross-section is a conceptual system diagram and does not describe ENEC’s internal plant systems or approved deployment geometry. The v4 simulation assumes flat 12 m depth, two guide bands with 11.8 m skirts, a 200 m modeled corridor, and powered wet collection/lift.
The optional bubble airlift / curtain is excluded from the 97.5% reference run. The project model estimated 77.1 kWh/event for continuous dual-line bubble operation and found no reliable capture gain across a very small repeat set; a field benefit is not established.
Jellyfish bubble-curtain tests have reported mixed field results and show that wave conditions can affect transport through a curtain: https://research.ucc.ie/en/publications/field-and-flume-tank-experiments-investigating-the-efficacy-of-a/ (Haberlin et al., 2021).
Bubble-curtain / wave-current physical interaction study: https://link.springer.com/article/10.1007/s10652-025-10029-1

## Slide 5
04 / OPERATING LOGIC
Automation inside hard limits
Start on an existing alert. Use local sensing to adjust the response, with operator oversight and independent fail-safe states.
01 / ALERT
ENEC bloom warning
Response window opens
→
02 / SENSE
Flux + flow + load
Local instruments confirm conditions
→
03 / ACT
Outer → second guide
Convey and lift within verified limits
→
04 / VERIFY
Receiver + escape count
Report delivered, held, and missed mass
CONTROL STACK
AI / ML (future, advisory)
Predict bloom flux and recommend activation or setpoints after site data exist. No trained ML/CV model is in the current simulation.
Local PLC + interlocks
Enforce depth, speed, pressure, load, and stop limits. Local operation remains available if communications fail.
Operator authorization
Supervised first deployment. Animal identification, handling, and release decisions follow an approved protocol.
MARLIN / ATP 2026 • ENEC CHALLENGE
05
Notes: The current simulation uses deterministic/synthetic control conditions and contains no trained machine-learning or computer-vision model. ML/CV appears here as a future decision-support feature, contingent on labeled local observations and validation.
The project’s operational concept uses local controls and independent limit checks so that communications loss does not cause uncontrolled actuator changes. Final setpoints and trips must be engineered and approved with ENEC.
Official challenge statement distinguishes post-alert management from early detection and invites environmental monitoring and decision support: https://challengeon.atrc.ae/en/challenges/atp2026/pages/enec-challenge-statement?lang=en

## Slide 6
05 / MODEL SCREENING
Strong reference case; clear stress-case misses
Bars show share delivered to the model’s hypothetical receiver—not biological survival or plant performance.
DELIVERED TO HYPOTHETICAL RECEIVING (%)
0
25
50
75
100
Reference • bubbles off
97.5%
2.5% uncaptured
Storm • 2 m waves / 14 m/s wind
84%
16% uncaptured
Strong cross-current sensitivity
93.5%
6.5% uncaptured
3× bloom arrival • capacity overload
41.7%
27% missed · 31.3% held
WHAT THIS SUPPORTS
The architecture is worth physical testing. The 95% delivery goal appears only in the synthetic reference case; wind, overload, cross-flow, common-cause misses, and depth change can break it.
27 numerical/invariant checks passed; zero mass-ledger error. These verify code consistency, not field physics.
MARLIN / ATP 2026 • ENEC CHALLENGE
06
Notes: All plotted results are from workbench/v4/output/RUN_REPORT.md. The model’s reference case has 97.50% delivered and 2.50% uncaptured; storm has 84% delivered and 16% uncaptured; strong transverse-current sensitivity has 93.5% delivered and 6.5% uncaptured; triple arrival has 41.67% delivered, 31.33% still held, and 27% uncaptured.
The 95% threshold is an aspirational screening target and is not achieved robustly across tested conditions.
The 27 tests check code/kinematics and mass balance. They do not establish full hydrodynamics, intake-system coupling, device capacity, ecological effect, or field catch rate.

## Slide 7
06 / ENVIRONMENTAL SAFEGUARDS
Protect the animals—and the flow around them
Treat ecological impact and hydraulic resistance as pass/fail gates, not as benefits assumed from a drawing.
01
Limit contact
Prefer open, smooth guidance surfaces and slow wet conveyance. Mesh, skirt, mooring, and shear choices need tank evidence.
02
Separate bycatch
Detect non-target organisms before handling; pause, isolate, and follow an ecologist-approved release protocol.
03
Protect water flow
Track differential pressure, flow change, line load, and clogging. Retract or bypass only within approved limits.
04
Close the ledger
Record delivered, held, escaped, bycatch, and unknown mass. No release direction is assumed safe without local flow checks.
STOP RULE
Unknown bycatch • rising load/pressure • failed sensor • unsafe sea state → isolate the section and alert the operator.
MARLIN / ATP 2026 • ENEC CHALLENGE
07
Notes: The official challenge requires minimizing potential harm to jellyfish and other marine organisms and considering unintended environmental consequences: https://challengeon.atrc.ae/en/challenges/atp2026/pages/enec-challenge-statement?lang=en
A large physical guide can introduce entanglement, debris, mooring, drag, and water-flow risks. The simulation does not model bycatch or injury, does not resolve detailed intake hydraulics, and does not establish a safe mesh or skirt design. The safeguards on this slide are proposed test gates, not demonstrated outcomes.

## Slide 8
07 / FEASIBILITY & COST
Spend energy only where it buys a measured benefit
The cost case is a design strategy now; site-specific capital and operating costs still need supplier quotes.
PASSIVE FIRST
Guide bands do the continuous interception; powered collection operates when a bloom response is active.
MODULAR
Segmented guides and independent collectors make inspection and repair local rather than system-wide.
NO ROBOT TAX IN THE MVP
Use an operator-supervised service craft during trials; defer an uncrewed vessel until it proves a labor or safety benefit.
BUBBLES ARE AN EVIDENCE-GATED OPTION
Not the core barrier
The current comparison does not show a dependable capture gain from continuous bubble operation.
77.1
kWh / bloom event
model estimate for two continuously operated diffuser lines; not a field energy measurement.
Test airlift and curtain independently in a flume; retain only if capture, ecology, and energy improve together.
MARLIN / ATP 2026 • ENEC CHALLENGE
08
Notes: The model’s bubble-on/off results are preliminary: bubble-on repeat range 2.25–2.50% uncaptured (n=4), bubble-off 2.00–2.50% (n=11). This is a small, model-dependent seed sample, not field evidence. Reported 77.1 kWh/event is an assumed compressor estimate for continuous operation of two lines.
Bubble curtain field/flume work found mixed results and identified wave conditions and jellyfish size/shape as important: https://research.ucc.ie/en/publications/field-and-flume-tank-experiments-investigating-the-efficacy-of-a/ (Haberlin, McAllen & Doyle, 2021, Aquaculture 531, 735915; DOI 10.1016/j.aquaculture.2020.735915).
No vendor pricing, anchor/installation quote, marine-service cost, or maintenance contract is included. The challenge asks for a cost-conscious approach; this slide proposes ways to limit unnecessary operating expense without claiming a validated total cost.

## Slide 9
08 / TEST PLAN
Prove the hard parts before a site pilot
Every gate should measure capture, marine impact, flow cost, and failure recovery together.
0
CALIBRATE
Bathymetry, ADCP current, intake-adjacent flow, bloom trajectories, and operator constraints.
ADVANCE WHEN
Site envelope signed off
1
FLUME
Guide geometry, airlift/bubble on-off, conveyor speed, clogging, escape, and bycatch handling.
ADVANCE WHEN
Target <5% escape in defined test envelope
2
SHELTERED SEA
Permitted deployment with ecological observation, load cells, pressure, flow, and recovery drills.
ADVANCE WHEN
Impact and hydraulic limits met
3
CONTROLLED DEMO
Operator-led demonstration under approved boundaries; no modification to plant or nuclear-safety systems.
ADVANCE WHEN
ENEC authorizes next step
Core measures
Escape % · bycatch / injury · pressure & flow change · kWh per tonne · staff-hours · recovery time · mass-balance closure
MARLIN / ATP 2026 • ENEC CHALLENGE
09
Notes: The challenge asks teams to explain how they would test or demonstrate the concept if shortlisted. The 5% escape threshold is a proposed engineering gate, not an established biological standard. Conditions for that target must be defined before testing and agreed with environmental specialists and the operator.
The challenge brief states no internal operational data or detailed facility design will be provided; public data and clearly stated assumptions may be used, with mentorship/clarification available to shortlisted teams: https://challengeon.atrc.ae/en/challenges/atp2026/pages/enec-challenge-statement?lang=en

## Slide 10
09 / ASSUMPTIONS & NEXT DECISIONS
A promising screen—not a promise
The model helps decide what to test next. It cannot yet certify a safe, 95% field outcome.
KEY ASSUMPTIONS
Synthetic bloom arrivals at 1,200 kg/h for four hours; not a public local abundance record.
12 m flat water depth, 200 m corridor, and guide contact probabilities of 0.90 / 0.80 are uncalibrated.
Weather and circulation use public regional reanalysis; forcing does not resolve local intake flow, turbulence, or guide feedback.
No validated ML/CV, bycatch/injury model, animal survival model, or field-tested handling/release protocol.
NEXT DECISION
Request a bounded technical review
Confirm deployment boundary, depth/current envelope, allowable flow change, marine-life review pathway, and approved response handling. Then calibrate the flume model and retest its worst cases.
Declaration: AI tools supported drafting and visual layout; the team reviewed the assumptions and owns the proposal.
SOURCES
ATP 2026 ENEC brief • Haberlin et al., Aquaculture (2021), DOI 10.1016/j.aquaculture.2020.735915 • Copernicus ERA5 / Marine ocean reanalysis
Public data are regional forcing inputs—not a jellyfish trajectory/abundance dataset and not site measurements.
MARLIN / ATP 2026 • ENEC CHALLENGE
10
Notes: Simulation details and caveats: workbench/v4/output/RUN_REPORT.md. Synthetic bloom loading, assumed 12 m flat water depth and 200 m corridor, uncalibrated contact probabilities, and no biological damage model or ML/CV model are in the simulation.
Challenge source and submission requirements: https://challengeon.atrc.ae/en/challenges/atp2026/pages/enec-challenge-statement?lang=en
Bubble-curtain jellyfish field/flume study: Haberlin, D., McAllen, R. & Doyle, T.K. (2021), Aquaculture 531, 735915. https://doi.org/10.1016/j.aquaculture.2020.735915
ERA5 hourly weather/wave reanalysis: https://cds.climate.copernicus.eu/datasets/reanalysis-era5-single-levels?tab=overview
Copernicus Marine Global Ocean Physics Reanalysis (GLORYS12V1): https://data.marine.copernicus.eu/?option=com_csw&product_id=GLOBAL_MULTIYEAR_PHY_001_030&view=details
These are broad public data products. Their use does not convert regional forcing into site-scale validation.